Hole Location Template 539AS-0207 PP, Rev A

Hole Location Template 539AS-0207 PP, Rev A

Hole Location Template 539AS-0207 PP, Rev A

Hole Location Template 539AS-0207 PP, Rev A

Hole Location Template 539AS-0207 PP, Rev A

Hole Location Template 539AS-0207 PP, Rev A

Hole Location Template 539AS-0207 PP, Rev A

Hole Location Template 539AS-0207 PP, Rev A

# Text boxes

Drop Tube Length Calculator

____________  = Measured distance from

top of riser pipe to

bottom of tank.

- 6 inches   =

.

=		  = Required length of

drop tube.

24th and Elm Street ( Dubuque, IA 52001

Ph: 800-553-4840  Fax: 563-583-5028

Email: custserv@morbros.com

539AS-0207 PP, Rev A

- Check drop tube.  This method is for a drop tube with an outside diameter of no more than 2”.

- Measure the distance from the top of the riser pipe to the bottom of the tank.

- Using the Drop Tube Length Calculator at right, calculate the length of the drop tube and cut the end of the drop tube square. (Cut end of drop tube should be 6 inches from bottom of tank.)

- Place the attached Hole Location Template onto the tube so the bottom edge of the sheet is flush with the bottom edge of the tube.

- Using the template, lightly punch hole locations and drill through the tube with a 7/32” drill.

- Remove the template from the drop tube.

- Place nut clips on tube and align with holes in tube.

- Place diffuser on tube, align holes and secure with enclosed screws.

INSTALLATION INSTRUCTIONS FOR 2” FIG. 539AS DIFFUSER

Drop Tube Length Calculator

____________  = Measured distance from

top of riser pipe to

bottom of tank.

- 6 inches   =

.

=		  = Required length of

drop tube.

24th and Elm Street ( Dubuque, IA 52001

Ph: 800-553-4840  Fax: 563-583-5028

Email: custserv@morbros.com

(Align this edge with bottom of tube)

Drill Hole (3x)

- Check drop tube. This method is for a drop tube with an outside diameter of no more than 2”.

- Measure the distance from the top of the riser pipe to the bottom of the tank.

- Using the Drop Tube Length Calculator at right, calculate the length of the drop tube and cut the end of the drop tube square. (Cut end of drop tube should be 6 inches from bottom of tank.)

- Place the attached Hole Location Template onto the tube so the bottom edge of the sheet is flush with the bottom edge of the tube.

- Using the template, lightly punch hole locations and drill through the tube with a 7/32” drill.

- Remove the template from the drop tube.

- Place nut clips on tube and align with holes in tube.

- Place diffuser on tube, align holes and secure with enclosed screws.

539AS-0207 PP, Rev A

(Align this edge with bottom of tube)

Drill Hole (3x)

Drill Hole (3x)

24th and Elm Street ( Dubuque, IA 52001

Ph: 800-553-4840  Fax: 563-583-5028

Email: custserv@morbros.com

INSTALLATION INSTRUCTIONS FOR 2” FIG. 539AS DIFFUSER

(Align this edge with bottom of tube)

(Align this edge with bottom of tube)

Drill Hole (3x)

(Align this edge with bottom of tube)

Drill Hole (3x)

(Align this edge with bottom of tube)

Drill Hole (3x)

(Align this edge with bottom of tube)

Drill Hole (3x)

(Align this edge with bottom of tube)

Drill Hole (3x)

539AS-0207 PP, Rev A

- Check drop tube. This method is for a drop tube with an outside diameter of no more than 2”.

- Measure the distance from the top of the riser pipe to the bottom of the tank.

- Using the Drop Tube Length Calculator at right, calculate the length of the drop tube and cut the end of the drop tube square. (Cut end of drop tube should be 6 inches from bottom of tank.)

- Place the attached Hole Location Template onto the tube so the bottom edge of the sheet is flush with the bottom edge of the tube.

- Using the template, lightly punch hole locations and drill through the tube with a 7/32” drill.

- Remove the template from the drop tube.

- Place nut clips on tube and align with holes in tube.

- Place diffuser on tube, align holes and secure with enclosed screws.

INSTALLATION INSTRUCTIONS FOR 2” FIG. 539AS DIFFUSER

Drop Tube Length Calculator

____________  = Measured distance from

top of riser pipe to

bottom of tank.

- 6 inches   =

.

=		  = Required length of

drop tube.