Hole Location Template 539AS-0405 PP

Hole Location Template 539AS-0405 PP

Hole Location Template 539AS-0405 PP

Hole Location Template 539AS-0405 PP

Hole Location Template 539AS-0405 PP

Hole Location Template 539AS-0405 PP

# Text boxes

INSTALLATION INSTRUCTIONS FOR 4” FIG. 539AS DIFFUSER

24th and Elm Street ( Dubuque, IA 52001

Ph: 800-553-4840 ( Fax: 563-583-5028

Drop Tube Length Calculator

____________  = Measured distance to

bottom of tank.

- 5 ½ inches  = Distance drop tube

will be from bottom

of tank.

=		  = Length drop tube is

to be cut to.

- Check drop tube: diffuser is made for a 4” drop tube with an inside diameter between 3-23/32” and 3-49/64”.

- Measure the distance to the bottom of the tank to the top of the drop tube.

- Using the Drop Tube Length Calculator at right, calculate the length of the drop tube and cut the end of the drop tube square. (Cut end of drop tube should be 5-6 inches from bottom of tank.)

- Place the attached Hole Location Template onto the tube so the bottom edge of the template is

flush with the bottom edge of the tube.

- Punch the locations of the holes using the template and drill through the tube with a 5/16” drill.

- Remove the template from the drop tube.

- Place diffuser on tube, align holes and secure with enclosed countersunk screws. Tighten screws until they are flush with the outer diameter of the drop tube.

24th and Elm Street ( Dubuque, IA 52001

Ph: 800-553-4840  Fax: 563-583-5028

Email: custserv@morbros.com

INSTALLATION INSTRUCTIONS FOR 4” FIG. 539AS DIFFUSER

539AS-0405 PP, Rev A

24th and Elm Street ( Dubuque, IA 52001

Ph: 800-553-4840  Fax: 563-583-5028

Email: custserv@morbros.com

Drop Tube Length Calculator

____________  = Measured distance to

bottom of tank.

- 5 ½ inches  = Distance drop tube

will be from bottom

of tank.

=		  = Length drop tube is

to be cut to.

- Check drop tube: diffuser is made for a 4” drop tube with an inside diameter between 3-23/32” and 3-49/64”.

- Measure the distance to the bottom of the tank to the top of the drop tube.

- Using the Drop Tube Length Calculator at right, calculate the length of the drop tube and cut the end of the drop tube square. (Cut end of drop tube should be 5-6 inches from bottom of tank.)

- Place the attached hole location template onto the tube so the bottom edge of the template is

flush with the bottom edge of the tube.

- Punch the locations of the holes using the template and drill through the tube with a 5/16” drill.

- Remove the template from the drop tube.

- Place diffuser on tube, align holes and secure with enclosed countersunk screws. Tighten screws until they are flush with the outer diameter of the drop tube.

24th and Elm Street ( Dubuque, IA 52001

Ph: 800-553-4840 ( Fax: 563-583-5028

24th and Elm Street ( Dubuque, IA 52001

Ph: 800-553-4840 ( Fax: 563-583-5028

- Check drop tube: diffuser is made for a 4” drop tube with an inside diameter between 3-23/32” and 3-49/64”.

- Measure the distance to the bottom of the tank to the top of the drop tube.

- Using the Drop Tube Length Calculator at right, calculate the length of the drop tube and cut the end of the drop tube square. (Cut end of drop tube should be 5-6 inches from bottom of tank.)

- Place the attached hole location template onto the tube so the bottom edge of the template is

flush with the bottom edge of the tube.

- Punch the locations of the holes using the template and drill through the tube with a 5/16” drill.

- Remove the template from the drop tube.

- Place diffuser on tube, align holes and secure with enclosed countersunk screws. Tighten screws until they are flush with the outer diameter of the drop tube.

Drop Tube Length Calculator

____________  = Measured distance to

bottom of tank.

- 5 ½ inches  = Distance drop tube

will be from bottom

of tank.

=		  = Length drop tube is

to be cut to.

539AS-0405 PP, Rev A

24th and Elm Street ( Dubuque, IA 52001

Ph: 800-553-4840  Fax: 563-583-5028

Email: custserv@morbros.com

INSTALLATION INSTRUCTIONS FOR 4” FIG. 539AS DIFFUSER

539AS-0405 PP, Rev A

(Align bottom of sheet with bottom of tube)

Drill Hole (3x)

Drill Hole (3x)

(Align bottom of sheet with bottom of tube)

Drill Hole (3x)

(Align bottom of sheet with bottom of tube)

Drill Hole (3x)

(Align bottom of sheet with bottom of tube)

Drill Hole (3x)

(Align bottom of sheet with bottom of tube)

Drill Hole (3x)

(Align bottom of sheet with bottom of tube)